The Ross XL-2200-FB (Heald Fixed Raptor) is part of a counter-intrusion system and is installed in open areas to prevent vehicular traffic.  Manufactured from heavy-duty steel with a corrosion-resistant galvanized finish, the fixed bollards are will last for years and provide crash-rated protection for a wide variety of applications.   Mounted in a very shallow foundation and tested as a single unit, the fixed bollards are tested to PAS 68:2013 with a classification of 7500 (N2) 48/90:0:0.  For more information, please call our toll-free number above or visit our website.

SECTION 323919

FIXED BOLLARDS

(Ross XL-2200-FB – HEALD FixeD RAPTOR)

GENERAL

SUMMARY

Work Included:  Provide labor, materials and equipment necessary to complete the work of this Section, including but not limited to the following:

Shallow-foundation fixed bollards.

SUBMITTALS

Product Data:  Submit manufacturer’s product data for each type of product.

Shop Drawings:  Submit shop drawings including the following:

Complete list of equipment, materials, and manufacturer’s descriptive and technical literature.

Proposed layout of foundation.

Reports and Certifications:  Submit the following:

Crash Test Rating:  PAS 68:2013 7500 (N2) 48/90:0:0.

Maintenance Manuals: Submit two copies of maintenance instructions.

Welder’s Certificates:  Copy of current certificate for AWS D1.1.

Warranty:  Submit executed copy of manufacturer’s warranty.

QUALITY ASSURANCE

Installer: Minimum 2 year documented history of installing similar equipment, authorized or certified by the manufacturer. Installer shall accept responsibility for all field verifications, underground utility locations.

Manufacturer’s Services:  If requested by the Owner, provide services of a manufacturer’s representative who is experienced in the installation of the bollards.

DELIVERY, STORAGE AND HANDLING

Store equipment in a location protected from the weather, humidity, temperature variation, dirt and dust, or other contaminants.  Store materials on sleepers or pallets and protect from rust and objectionable materials such as dirt, grease or oil.

WARRANTY

Warranty:  Provide manufacturer’s standard limited warranty.

PRODUCTS.

MANUFACTURER

Basis-of-Design Manufacturer:  Ross Technology Company, 104 North Maple Avenue, Leola, PA 17540.  Toll-free 800-345-8170.  www.rosstechnology.com.  No substitutions.

FIXED BOLLARDS

Fixed Shallow-Mount Bollards: Ross XL-2200-FB (Heald Fixed Raptor) by Ross Technology Company complying with the following:

Performance:  Crash tested as a single unit in accordance with PAS 68:2013 and assigned a classification of PAS 68:2013 7500 (N2) 48/90:0:0 (7500 kg 2-axle truck at 48 kph (30 mph) at 90 degree impact angle, with zero penetration).

Bollard Assembly: Single unit, constructed from heavy-duty structural steel sections.  Supplied fully finished, with all components required for installation.

Height:  38.8 inches (985 mm).

Foundation Depth:  7.9 inches (200 mm).

Foundation Width:  63 inches (1600 mm).

Bollard Width:  7.9 inches (200 mm).

Concrete Foundation: 5000 psi (34.5 MPa) Portland Type 1 concrete with an industry standard cure time of 28 days. Normal maximum aggregate size shall be 1.5 inches (38 mm).  Vibrate concrete to fill all voids. Rebar shall comply with ASTM A615 grade 60.

Finish:

Hot-dip galvanized per ASTM A123.

[Option] Wash primer after hot-dip galvanizing per ASTM A123.

[Option] Factory wash primer and finish after hot-dip galvanizing per ASTM A123; polyurethane top coat.  Select colors from manufacturer’s color range.

[Option] Decorative covers.

[Option] Reflective striping.

EXECUTION

EXAMINATION

Examine substrates and site conditions for compliance with requirements for installation tolerances and other conditions affecting performance.  Proceed with installation only after unsatisfactory conditions have been corrected.

INSTALLATION

Install products in strict accordance with manufacturer’s instructions and approved submittals.  Locate units level, plumb, and in proper alignment with adjacent work. Use concealed anchorages where possible.

Excavate to required depth and place concrete in accordance with ACI standards

Protect adjacent areas against damage; repair or patch damaged areas.  Restore damaged finishes so no evidence remains of corrective work.

CLEANING

Clean exposed surfaces using methods acceptable to the manufacturer which will not damage finish.

END OF SECTION

Rev 0719 sk